## Slide 1
Machine Learning with Multiscale Dataflow Computing for High Energy Physics
10.7.2019

## Slide 2
Outline
Dataflow Concept and Maxeler
Dataflow for ML and Use Cases
Dataflow Programming Introduction
Hands-on Example
2

## Slide 3
Dataflow Concept and Maxeler
10.7.2019

## Slide 4
Programmable Spectrum
4
Multi-Core
Several-Cores
Dataflow
Intel, AMD
GPU (NVIDIA, AMD)
Tilera, XMOS etc...
Maxeler
Hybrid e.g. AMD Fusion, IBM Cell
Control-flow processors
Dataflow processor
Increasing Parallelism (#cores)
Increasing Core Complexity ( Hardware Clock Frequency )
Many-Cores
GK110
Single-Core CPU

## Slide 5
MaxRing
Interconnect
Dataflow Engine (DFE)
LMEM (Large Memory)
4-96GB
Reconfigurable compute fabric
Dataflow cores & FMEM (fast memory)
High bandwidth memory link
Link to main data network
MaxRing links
Largest Reconfigurable Chip
O(1k) multipliers
O(100k) logic cells
O(10MB) of on-chip SRAM
O(10GB) of on-card DRAM*
DFE-to-DFE interconnect
* approaching 128GB on a ¾, single slot PCIe card
5
Maxeler Dataflow Engines (DFEs)

## Slide 6
Maxeler Dataflow Engines (DFEs)
6
DFE
(Dataflow Engine)
CPU

## Slide 7
Control Flow versus Data Flow
Control Flow:
  It is all about how instructions “move”
  Data may move along with instructions (secondary issue)
  Order of computation is the key
Data Flow:
  It is about how data moves through a set of “instructions” in 2D space
  Data moves will trigger control
  Data availability, transformations and operation latencies are the key
7

## Slide 8
Area Utilisation of Modern Chips
8
AMD Bulldozer CPU
Nvidia Tesla V100 GPU

## Slide 9
DFE Area Utilisation
9

## Slide 10
Dataflow Computing
A custom chip for a specific application
No instructions ➝ no instruction decode logic
No branches ➝ no branch prediction
Explicit parallelism ➝ no out-of-order scheduling
Data streamed onto-chip ➝ no multi-level caches
10
My Dataflow Engine
(Lots of) Memory
Rest of the world

## Slide 11
Dataflow Computing
Single worker builds a single bicycle from a group of parts
All operations must be done in sequence by the single worker
The worker expends/wastes a lot of time getting and selecting parts
11
Each component is added to the bicycle in a production line.
All operations happen in parallel with many workers
Only one types of parts needs to be delivered to each worker

## Slide 12
MaxCompiler: Dataflow Programming
12

## Slide 13
FPGA vs Dataflow
Current DFEs are implemented using FPGA technology
  Maxeler MAX4C, MAX4N, MAX5C
  Xilinx Alveo
  Amazon EC2 F1 instance
FPGA development for HPC often focused on kernels
  E.g. accelerate matrix multiply, FFT, convolution
This often ignores I/O and memory bottlenecks
Dataflow looks at the complete application
  Optimise Dataflow
  Reduce Bandwidth requirements
  Optimise throughput
13

## Slide 14
CPU
DFE
Function1 – 5s
Function2 – 1s
CPU
Function1 – 1,000s
Function2 – 1s
10G data transferred
Transfer 5s
CPU
DFE
Function1 – 5s
Function2 – 2s
Final result only
CPU time 1,001s
Option 1 time 11s
Option 2 time 7s
Some observations
At Kernel level:
        Kernel 1 speedup 200x (!)
Kernel 2 “speedup” 0.5x (!)
At System level:
Option 1 (Kernel 1 only) speedup 91x
Option 2 (Kernels 1 and 2) speedup 143x
But what about the required effort?
14
Decelerate to Accelerate

## Slide 15
SIMULATE AND DEBUG
GENERATE DATAFLOW
PROGRAM
ARCHITECT
ANALYSE
Used to build balanced real systems, however, not easy to learn/educate
OK?
many hours …
Custom HW
Non Traditional Design Process
Notes: Even better: the functions moved to the edge are fixed and do not change quite often --> HW

## Slide 16
MaxRing
Interconnect
Dataflow Engine (DFE)
LMEM (Large Memory)
4-96GB
Reconfigurable compute fabric
Dataflow cores & FMEM (Fast Memory)
High bandwidth
memory link
Link to main data network
(e.g., PCIe, Infiniband)
MaxRing links
+
{
Application and MaxJ
gen4
gen5
Performance Portable Migration
(MAX4 Intel based)
(MAX5 Xilinx based)
Multiple Platforms - Single Abstraction

## Slide 17
Maxeler Dataflow Software Ecosystem
17
http://appgallery.maxeler.com

## Slide 18
Over 150 Maxeler University Program Members
18

## Slide 19
Dataflow for ML and Use Cases
10.7.2019

## Slide 20
CNN Inference on DFEs
ICCD 2017: N. Voss et al: Convolutional Neural Networks on Dataflow Engines
High throughput implementation of VGG-16
~84.5 images/sec (224x224 pixels), 2.45 TOP/s
20
We made further improvements:
  Support for generic CNNs
  All input image sizes supported (up to 10K images)
  Higher Speed
  Available on MAX5C, Alveo and Amazon F1

## Slide 21
CNN Traning on DFEs
21

## Slide 22
Dataflow vs GPU for ML
Advantages:
  Predictable, guaranteed low latency
  Low power usage
  Fully custom types
    E.g. binary or ternary networks possible
    But also 20 bit if required
  Can be fed directly from networking connections
    No bottleneck of getting data from network via CPU and PCIe to the GPU
  Lower cooling and space requirements
Disadvantages:
  Currently not fully integrated into common ML libraries
    More development effort required
22

## Slide 23
Triggering at CMS
Study by PhD student at imperial
  Reimplement triggering algorithm using MaxJ
23
 | VHDL | MaxJ
LUTs | 95,235 | 102,508
Slice Regs. | 153,198 | 130,072
DSPs | 288 | 288
BRAM tiles | 0 | 0
Lines of Code | 3,000 | 1,000
Developer Experience | 10+ years | < 1 year

## Slide 24
Kalman Filter
Study by PhD student at imperial
  Implement Kalman Filter using MaxJ
  Implemented in Fixed Point
  36 instances per Virtex 7 FPGA with 230ns latency per iteration
Second group:
  Worried that Kalman Filter to complicated for FPGA
  -> Simplified math
  Implement linear regression in VHDL
  Took longer than MaxJ effort
Result: Complicated maths in MaxJ > easy maths in VHDL
24

## Slide 25
EU PRACE PCP
Delivered to Jülich in 2017
EU funded
Ported for applications
  Quantum ESPRESSO (Quantum Chemistry)
  Berlin QCD (Quantum Chromodynamics)
  NEMO (Ocean Modelling)
  SPECFEM3D (Seismic Modelling)
Target: 20-50x better performance density
25

## Slide 26
BQCD
Run CG of any size on a single DFE, with highly accurate results
  Custom numerics in 24bit fixed point
Setup for BQCD:
  Target system: 11 MPC-X nodes (88 DFEs) and 24 AMD EPYC nodes
  Speedup on compute per volume basis, for 1 PFlop/s performance:
    38x CG only; 18x whole application
26

## Slide 27
Radiotherapy
Radiotherapy: Cancer treatment using radiation
Target: Real time (< 1s) Monte Carlo simulation of dose accumulation
  Enables adaptive treatment
    Reduces overall dose delivered to patient
Managed to achieve a speedup of over 8x compared to GPUs
Real time simulation possible using three FPGA cards
Paper will be presented next week at ASAP conference
27

## Slide 28
Future Project: XFEL
We are currently planning a project with European XFEL
Target:
  Enable real-time visualisation of sensor output
  Use 4 DFEs to perform data calibration
  First only for the AGIPD detector
28

## Slide 29
Dataflow Programming Introduction
10.7.2019

## Slide 30
Dataflow Graph
a = b * (c + b * d)
30
d
c
b
x
+
x
a

## Slide 31
MaxJ Intro: Programming
Example: x2 + 30
31
DFEVar x = io.input("x", dfeInt(11));
DFEVar result = x * x + 30;
io.output("y", result, dfeInt(11));
x
x
+
30
y

## Slide 32
MaxJ Intro: What is a DFEVar?
A connection between operators in the dataflow graph
An edge in the dataflow graph
A stream of data elements of a certain type and size
Physically it is a set of wires in the hardware
It looks like a variable in MaxJ code
IT IS NOT A VARIABLE! (in the traditional CS sense)
32

## Slide 33
You can use the full power of Java to write a program that generates the dataflow graph
Java variables can be used as constants in hardware
  int y; DFEVar x; x = x + y;
Hardware variables can not be read in Java!
  Cannot do: int y; DFEVar x; y = x;
Java conditionals and loops choose how to generate hardware → not make run-time decisions
Once you execute your Java program the generated graph is what exist in your application (not the Java)
We do not execute Java on the DFE!
MaxJ Intro: Java meta-programming
33

## Slide 34
MaxJ Intro: Dataflow Graph Generation
34
DFEVar x = io.input(“x”, type);
DFEVar y;
y = x + 1;
io.output(“y”, y, type);
x
+
1
y

## Slide 35
MaxJ Intro: Dataflow Graph Generation
35
x
x
y
+
DFEVar x = io.input(“x”, type);
DFEVar y;
y = x * x + x;
io.output(“y”, y, type);

## Slide 36
MaxJ Intro: Dataflow Graph Generation
36
What’s the value of h if we stream in 1?
DFEVar h = io.input(“h”, type);
int s = 2;
s = s + 5
h = h + 10
h = h + s;
What’s the value of s if we stream in 1?
DFEVar h = io.input(“h”, type);
int s = 2;
s = s + 5
h = h + 10
s = h + s;
+
+
10
h
7
18
Compile error.
You can’t assign a hardware value to a Java int

## Slide 37
MaxJ Intro: Dataflow Graph Generation
37
What dataflow graph is generated?
DFEVar x = io.input(“x”, type);
int s = 10;
DFEVar y;
if (s < 100) { y = x + 1; }
else { y = x – 1; }
io.output(“y”, y, type);
What dataflow graph is generated?
DFEVar x = io.input(“x”, type);
DFEVar y;
if (x < 10) { y = x + 1; }
else { y = x – 1; }
io.output(“y”, y, type);
x
+
1
y
Compile error.
You can’t use the value of ‘x’ in a Java conditional

## Slide 38
MaxJ Intro: Dataflow Graph Generation
38
DFEVar x = io.input(“x”, type);
DFEVar y = x;
for (int i = 1; i <= 3; i++) {
y = y + i;
}
io.output(“y”, y, type);
Can make the loop any size – until you run out of space on the chip!
Larger loops can be partially unrolled in space and reused multiple times in time
x
+
1
y
+
2
+
3

## Slide 39
You describe a dataflow graph generation using Java syntax
Objects in the MaxCompiler API are used to generate hardware or configure the hardware/the build process
Java API is crafted to ease the generation of massive dataflow graphs
  Object Orientation is possible and encouraged (e.g. using KernelLibs)
  You can write generic code which optimises itself on the fly
  You can write optimisation libraries, e.g., MaxPower
  Many normal Java libraries can be used, e.g., JUnit
MaxJ Intro: Java meta-programming
39

## Slide 40
MaxJ Intro: Example: Moving Average
40
class MovingAvgKernel extends Kernel {
MovingAvgKernel() {
DFEVar x = io.input(“x”, dfeFix(24,12));
DFEVar prev = stream.offset(x, -1);
DFEVar next = stream.offset(x, 1);
DFEVar sum = prev + x + next;
DFEVar result = sum / 3;
io.output(“y”, result, dfeFix(24,12));
}
}

## Slide 41
The dataflow graph in a kernel is statically scheduled and will be executed simultaneously in a parallel fashion
Operations have inherent latencies
  If different data paths meet, they need to be balanced and delays are inserted
  The scheduler tries to minimise the costs of implementing those delays
  You can add manual scheduling constraints with stream.offset()
MaxJ Intro: Scheduling
41

## Slide 42
MaxJ Intro: Scheduling
42
DFEVar x = io.input(“x”, type);
DFEVar y;
y = (x + x) * x;
io.output(“y”, y, type);
x
+
y
x
1

## Slide 43
MaxJ Intro: Scheduling
43
DFEVar x = io.input(“x”, type);
DFEVar y;
y = (x + x) * stream.offset(x, 1);
io.output(“y”, y, type);
x
+
y
x

## Slide 44
MaxJ Intro: Control in Space
44
class SimpleKernel extends Kernel {
SimpleKernel() {
DFEVar x = io.input(“x”, dfeFix(24,12));
DFEVar result = (x>10) ? x+1 : x-1;
io.output(“y”, result, dfeFix(24,12));
}
}
x
+
1
y
-
1
>
10
mux

## Slide 45
Operations instantiated as separate arithmetic units
Units along data paths use custom arithmetic and numeric representations (as long data stays correct)
These custom number formats may reduce individual unit sizes (and increase the number of parallel units that can fit into a given DFE)
Data rates of memory and I/O communication are also typically increased due to reduced data sizes
MaxJ Intro: Spatial Arithmetic
45

## Slide 46
MaxJ Intro: Optimisations at all levels
46
Multiple scales of computing | Important features for optimization
complete system level | balance compute, storage and IO
parallel node level | maximize utilization of compute and interconnect
microarchitecture level | minimize data movement
arithmetic level | tradeoff range, precision and accuracy = discretize in time, space and value
bit level | encode and add redundancy

## Slide 47
MaxJ Intro: Development Process
47
Original Application
Identify code for acceleration and analyze bottlenecks
Write MaxCompiler code
Simulate
Functions correctly?
Build DFE
Integrate with CPU code
Meets performance goals?
Accelerated Application
NO
YES
YES
NO
Transform app, architect and model performance
Start

## Slide 48
MaxJ Intro: Build Process
48
Host Application *.c, *.f90 ...
User Input
Compiler
Linker
Executable
Output
.max File
Sim or H/W
(.max)
MaxCompiler
Output
MyKernel.maxj
MyManager.maxj
MaxIDE
Rewrite only DFE- migrating code
MaxelerOS
Library
SLiC
Library

## Slide 49
MaxJ Intro: Application Components
49
SLiC
MaxelerOS
Memory
CPU
Memory
PCI Express
Kernels (MaxJ)
(instantiate the arithmetic structure)
Manager (MaxJ)
(arrange the data orchestration)
Host application (C, Python, Matlab..)

## Slide 50
MaxJ Intro: Parts to create a DFE
50
CPU Code
Manager Code
Kernel Code

## Slide 51
MaxCompiler – Java-driven dataflow compiler
SLiC Interface – CPU integration
MaxelerOS – optimized DFE <-> CPU link
Seamless simulation environment
MaxJ Intro: Programming Components
51

## Slide 52
MaxJ Intro: Simple Application Example
52
int*x, *y;
for (int i =0; i < DATA_SIZE; i++)
y[i]= x[i] * x[i] + 30;
Main
Memory
CPU
CPU
Code
Host Code (.c)

## Slide 53
MaxJ Intro: Simple Application Example
53
PCI
Express
Manager
DFE
Memory
MyManager (.maxJ)
Main
Memory
CPU
CPU
Code
Host Code (.c)
SLiC
MaxelerOS
y
x
x
+
30
y
x
int*x, *y;
MyKernel( DATA_SIZE,
x, y, DATA_SIZE*4);
Manager m = new Manager();
Kernel k =
new MyKernel();
m.setKernel(k);
m.setIO(
link(“x", CPU),
link(“y", CPU));
m.build();
DFEVar x = io.input("x", dfeInt(32));
DFEVar result = x * x + 30;
io.output("y", result, dfeInt(32));
MyKernel (.maxJ)

## Slide 54
MaxJ Intro: Simple Application Example
54
PCI
Express
Manager
DFE
Memory
MyManager (.maxJ)
Main
Memory
CPU
CPU
Code
Host Code (.c)
SLiC
MaxelerOS
x
x
+
30
y
x
int*x, *y;
MyKernel( DATA_SIZE,
x, y, DATA_SIZE*4);
Manager m = new Manager();
Kernel k =
new MyKernel();
m.setKernel(k);
m.setIO(
link(“x", CPU),
link(“y", DRAM_LINEAR1D));
m.build();
DFEVar x = io.input("x", dfeInt(32));
DFEVar result = x * x + 30;
io.output("y", result, dfeInt(32));
MyKernel (.maxJ)

## Slide 55
Dataflow Programming Introduction:
Kernels
10.7.2019

## Slide 56
Kernels: The Full Kernel
Example: x2 + 30
56
public class MyKernel extends Kernel {
public MyKernel (KernelParameters parameters) {
super(parameters);
DFEVar x = io.input("x", dfeInt(11));
DFEVar result = x * x + 30;
io.output("y", result, dfeInt(11));
}
}
x
x
+
30
y

## Slide 57
Kernels: Streaming Data
57

## Slide 58
Kernels: Streaming Data
58

## Slide 59
Kernels: Streaming Data
59

## Slide 60
Kernels: Streaming Data
60

## Slide 61
Kernels: Streaming Data
61

## Slide 62
Kernel: What about Moving Average
62
class MovingAvgKernel extends Kernel {
MovingAvgKernel() {
DFEVar x = io.input(“x”, dfeFix(24,12));
DFEVar prev = stream.offset(x, -1);
DFEVar next = stream.offset(x, 1);
DFEVar sum = prev + x + next;
DFEVar result = sum / 3;
io.output(“y”, result, dfeFix(24,12));
}
}

## Slide 63
Kernel: What about Moving Average
63

## Slide 64
Kernel: What about Moving Average
64

## Slide 65
Kernel: What about Moving Average
65

## Slide 66
Kernel: What about Moving Average
66

## Slide 67
Kernel: What about Moving Average
67
What about the boundary cases?

## Slide 68
MaxJ Intro: Conditionals
68
Data dependent conditional statements are extremely common
For example, How can we implement this in MaxJ?
int C = 500;
for (int i = 0; i < N; i++) {
if (x[i] > y[i])
result[i] = x[i] – y[i];
else
result[i] = C + x[i] + y[i];
}

## Slide 69
MaxJ Intro: Conditionals
69
DFEVar x = io.input("x", type);
DFEVar y = io.input("y", type);
DFEVar C = io.scalarInput("C", type);
DFEVar result = x > y ?
(x - y) : (C + x + y);
OR:
DFEVar result = control.mux(x > y,
C + x + y, x – y);
The second option also allows for more than two inputs
x
-
y
+
+
C
>
Mux
Select
false
true

## Slide 70
MaxJ Intro: Working with loop counters
70
How can we implement this in MaxCompiler?
for (int i = 0; i < N; i++) {
q[i] = p[i] + i;
}
How about this?
DFEVar p = io.input(“p”, dfeInt(32));
DFEVar i = io.input(“i”, dfeInt(32));
DFEVar q = p + i;
io.output(“q”, q, dfeInt(32));
Yes…. But, now we need to create an array i in software and send it to the DFE as well
d
+
q
i

## Slide 71
MaxJ Intro: Working with loop counters
71
There is very little ‘information’ in the i stream.
  Could compute it directly on the DFE itself
DFEVar p = io.input(“p”, dfeInt(32));
DFEVar i = control.count.simpleCounter(32, N);
DFEVar q = p + i;
io.output(“q”, q, dfeInt(32));
Counters can be used to generate sequences of numbers
Complex counters can have strides, wrap points, triggers:
  E.g. if (y==10) y=0; else if (en==1) y=y+2;
Half as many inputs
Less data transfer
d
+
q
cnt

## Slide 72
Kernel: What about Moving Average
72
What about the boundary cases?

## Slide 73
Kernel: Moving Average Boundaries
73
What about the boundary cases?
To handle the boundary cases, we must explicitly code special cases at each boundary

## Slide 74
Kernel: What about Moving Average
74

## Slide 75
Stream inputs/outputs process arrays
  Read and write a new value each cycle
  Off-chip data transfer required: O(N)
Counters can compute intermediate streams on-chip
  New value every cycle
  Off-chip data transfer required: None
Compile time constants can be combined with streams
  Static value through the whole computation
  Off-chip data transfer required: None
What about something that changes occasionally?
  Don’t want to have to recompile → Scalar input
  Off-chip data transfer required: O(1)
Kernel: Scalar Inputs
75

## Slide 76
Consider
void fn1(int N, int *q, int *p) {
for (int i = 0; i < N; i++)
q[i] = p[i] + 4;
}
Vs
void fn2(int N, int *q, int *p, int C) {
for (int i = 0; i < N; i++)
q[i] = p[i] + C;
}
In fn2, we can change the value of C without recompiling, but it is constant for the whole loop
MaxCompiler equivalent:
DFEVar p = io.input(“p”, dfeInt(32));
DFEVar C = io.scalarInput(“C”, dfeInt(32));
DFEVar q = p + C;
io.output(“q”, q, dfeInt(32));
A scalar input can be changed once per stream, loaded into the chip before computation starts.
Kernel: Scalar Inputs
76
d
+
q
C
Written by host

## Slide 77
Things that do not change every cycle, but do change sometimes and we do not want to rebuild the .max file.
Constants in expressions
Flags to switch between two behaviours
  result = enabled ? x + 7 : x;
Control parameters to counters, e.g. max, stride, etc
  if (cnt==cnt_max) cnt=0; else cnt = cnt + cnt_step;
Kernel: Scalar Input Use Cases
77

## Slide 78
The chip in a DFE has a few MB of very fast block RAM
Can be used to explicitly store data on chip:
  Lookup tables
  Temporary Buffers
Mapped ROMs/RAMs can also be accessed by host
Kernel: On-chip Memories
78
for (i = 0; i < N; i++) {
q[i] = table[ p[i] ];
}
DFEVar p = io.input(“p”, dfeInt(10));
DFEVar q = mem.romMapped(“table”, p, dfeInt(32), 1024);
io.output(“q”, q, dfeInt(32));
d
q
Mapped ROM table
Written by host

## Slide 79
In general we have streams, ROMs (tables) and scalars
Use the most appropriate mechanism for the type of data and required host access speed.
Stream inputs/outputs can operate for a subset of cycles using a control signal to turn them on/off
Kernel: Getting Data In and Out
79
Type | Size (items) | Host write speed | Chip area cost
Scalar input/output | 1 | Slow | Low
Mapped memory (ROM / RAM) | Up to a few thousand | Slow | Moderate
Stream input/output | Thousands to billions | Fast | Highest

## Slide 80
Kernel: Stream Loop
80
uint A[...]; uint B[...];
for (int count=0; ; count += 1)
B[count] = A[count] + 1;
DFEVar A = io.input(”input” , dfeUInt(32));
DFEVar B = A + 1;
io.output(”output” , B , dfeUInt(32));
A
+
1
B

## Slide 81
Kernel: Stream Loop with Counter
81
A
+
B
count
for (int count = 0; count < N ; count += 1)
B[count] = A[count] + count;
DFEVar A = io.input(”input” , dfeUInt(32));
DFEVar count = control.count.simpleCounter(32,N);
DFEVar B = A + count;
io.output(”output” , B , dfeUInt(32));
If the array subscripts are more complicated, you need to think about how to generate addresses for the DRAM

## Slide 82
Kernel: Nested Loops
82
int count = 0;
for (int i=0; i<N; ++i) {
for (int j=0; j<M; ++j) {
B[count] = A[count]+(i*M)+j;
count += 1;
}
}
DFEVar A = io.input(”input” , dfeUInt(32));
CounterChain chain = control.count.makeCounterChain();
DFEVar j = chain.addCounter(M, 1).cast(dfeUInt(32));
DFEVar i = chain.addCounter(N, 1).cast(dfeUInt(32));
DFEVar B = A + i*100 + j;
io.output(”output” , B , dfeUInt(32));
A
+
B
j
100
i
+
*

## Slide 83
for (i = 0; ; i += 1) {
float d = input[i];
float v = 2.91 – 2.0*d;
for (iter=0; iter < 4; iter += 1)
v = v * (2.0 - d * v);
output[i] = v;
}
DFEVar d = io.input(”d”, dfeFix(24,12));
DFEVar TWO = constant.var(dfeFix(24,12), 2.0);
DFEVar v = constant.var(dfeFix(24,12), 2.91) − TWO*d;
for ( int iteration = 0; iteration < 4; iteration += 1) {
v = v*(TWO− d*v);
}
io.output(”output” , v, dfeFix(24,12));
Kernel: Unrolling with Dependence
83
The software loop has a cyclic dependency (v)
But the unrolled datapath is acyclic

## Slide 84
Kernel: Variable Length Loop
84
for (count=0; ; count += 1) {
int d = input[count];
int shift = 0;
while (d != 0 && ((d & 0x3FF) != 0x291)) {
shift = shift + 1;
d = d >> 1;
}
output[count] = shift;
What do we do with a while loop (or a loop with a “break”)?
// converted to fixed length
for (count=0; ; count += 1) {
int d = input[count];
int shift = 0;
bool finished = false;
for (int i = 0; i < 22; ++i) {
bool condition = (d != 0 && ((d & 0x3FF) != 0x291));
finished = condition ? true : finished; // loop-carried
shift = finished ? shift : shift + 1; // dependencies
d = d >> 1;
}
output[count] = shift;
}
Count | Condition | Finished | Shift
1 | f | f | 1
2 | f | f | 2
3 | f | f | 3
4 | f | f | 4
5 | t | t | 5
6 | f | t | 5
7 | f | t | 5
8 | f | t | 5
9 | F | t | 5
Find maximum number of iterations
Execute all of them
Use bool to keep track of loop condition and keep result

## Slide 85
Kernel: Variable Length Loop in HW
85
for (count=0; ; count += 1) {
int d = input[count];
int shift = 0;
bool finished = false;
for (int i = 0; i < 22; ++i) {
bool condition=(d!=0&&((d&0x3FF)!=0x291));
finished = condition ? true : finished;
shift = finished ? shift : shift + 1;
d = d >> 1;
}
output[count] = shift;
}
DFEVar d = io.input(”d”, dfeUInt(32));
DFEVar shift = constant.var(dfeUInt(5), 0);
DFEVar finished = constant.var(dfeBool(), 0);
for ( int i = 0; i < 22; ++i) { // unrolled
DFEVar condition = d.neq(0)&((d&0x3FF).neq(0x291));
finished = condition ? constant.var(1) : finished ;
shift = finished ? shift : shift + constant.var(1);
d = d >> 1;
}
// Output
io.output(”output” , shift , dfeUInt(5));

## Slide 86
Kernel: To Unroll or Not To Unroll
86
Loop Unrolling
  Gets rid of loop-carried dependency by creating a long pipeline
  Requires O(N) space on the chip...what if it does not fit?
  If we can’t unroll, we end up with a cycle in the dataflow graph
  We need to make sure the cycle in the graph is compatible with the pipeline depth
Variable-length loop (with loop-carried dependency)
  Can be fully unrolled, BUT need to know maximal number of iterations
  Utilization depends on actual data...
  What if max iterations is much larger than average? Or max is not known? Or max iterations don’t fit on the chip?

## Slide 87
Dataflow Programming Introduction:
CPU Integration
10.7.2019

## Slide 88
CPU: Application Execution
88
Application
1
Application done!
I’m ready to run it...
CPU
2
MaxelerOS allocates a DFE
MaxelerOS
PCIe, InfiniBand
DFE
DFE
3
DFE is configured using .max-file
DFE
4
DFE is Ready to use
.max
file

## Slide 89
CPU: Exportable DFE Configurations
89
CPU
CPU Memory
DFEs
DFE Memory
Interconnect
C / Python / MATLAB / etc program
.max
file
MaxCompiler
.max file
collection

## Slide 90
Either
  DFE configuration data
  DFE simulation model
DFE Interface Info
  e.g. List of CPU settable values, number and names of I/O streams, etc.
CPU function code providing APIs specific to the .max file
CPU: .max File Contents
90

## Slide 91
Simple Live CPU Interface:
  Combination of fixed software function calls and MaxCompiler-generated code for interacting with DFEs
By default all functions in all layers can be used from C
SLiC has a layered interface:
  Basic Static – Single function-call to execute and complete a compute action on any appropriate DFE available
  Advanced Static – Can be more specific about which DFE to use and enables use of multiple DFEs at once
  Advanced Dynamic – Remove dependency on generated code from MaxCompiler in .max file for maximum flexibility
CPU: SLiC Interface
91

## Slide 92
Enable SLiC calls across many languages:
  Currently: C/C++, Python, MATLAB, R, Haskell
  Upcoming: Java, Excel
Every .max-file usable from any supported language
CPU: Skins
92
.max file
SLiC-Compile
tool
MATLAB:
.mex + .m
C/C++:
.o
R:
.tar.gz
Python:
.py + .so
Haskell:
.o + .hi

## Slide 93
Simple example computation
z[i] = a × (y[i-1]+y[i]+y[i+1])+ x[i]
2 input streams, 1 input scalar, 1 output stream
CPU: Example
93
public class ConvolveKernel extends Kernel {
static DFEType type = dfeFix(24,12);
public ConvolveKernel(KernelParameters parameters) {
super(parameters);
DFEVar x = io.input("x", type);
DFEVar y = io.input("y", type);
DFEVar a = io.scalarInput("a", type);
DFEVar conv = stream.offset(y,-1) + y
+ stream.offset(y,+1);
DFEVar z = a*conv + x;
io.output("z", z, type);
}
}
x
+
z
a
y
+
+1
-1
×
+

## Slide 94
CPU: Example
94
#include “Convolve.h"
#include "MaxSLiCInterface.h"
int main(void)
{
const int size = 384;
int sizeBytes = size * sizeof(float);
float *x, *y, *z1, *z2;
int coeff1 = 3, coeff2 = 5;
printf("Generating data...\n");
// Allocate x,y,z of sizeBytes
// Initialize x, y data
printf("Convolving on DFE...\n");
Convolve(size, coeff1, x, y, z1);
Convolve(size, coeff2, x, z1, z2);
printf("Done.\n");
return 0;
}
public class ConvolveManager {
public static void main(String[] args) {
// Create kernel and manager
EngineParameters p = new EngineParameters(args);
Manager m = new Manager(p);
Kernel k = new ConvolveKernel(
m.makeKernelParameters());
// Set-up kernel I/O to/from CPU
m.setKernel(k);
m.setIO(
link("x", IODestination.CPU),
link("y", IODestination.CPU),
link("z", IODestination.CPU));
// Auto-generate simple SLiC interface
m.createSLiCinterface();
m.build();
}
}
SLiC function generated in MaxFile
void Convolve(int32_t param_N, double inscalar_ConvolveKernel_a,
const float* instream_x, const float* instream_y,
float* outstream_z);

## Slide 95
Dataflow Programming Introduction:
HW Compilation
10.7.2019

## Slide 96
Compilation: Graphs to DFE hardware
96
.maxj
Files
MaxCompiler
Chip
Vendor Tools
1
HDL
Files
DFE Generator
Executable
.max
File
Design your kernels with MaxCompiler
2
Compile Using MaxCompiler
3
A Java Executable is Generated
4
Running the Executable first
Generates HDL
5
Then, it calls the
chip vendor tools
6
Final output is generated
* Fully Automated

## Slide 97
Compilation: Chip Vendor Back-End
97
Mon 16:27: MaxCompiler version: 2012.2
Mon 16:27: Build “MyKernel" start time: Mon Apr 08 16:27:24 BST 2013
Mon 16:27: Main build process running as user training1 on host Maxworkstation7478
Mon 16:27: Build location: /home/training1/maxcompiler-builds/MyKernel
Mon 16:27: Instantiating manager
Mon 16:27: Instantiating kernel “MyKernel"
Mon 16:27: Compiling manager (CPU I/O Only)
Mon 16:27: Compiling kernel "MyKernel"
Mon 16:27: Generating input files (VHDL, netlists, CoreGen)
Mon 16:27: Running back-end build (12 phases)
Mon 16:27: (1/12) - Prepare MaxFile Data (GenerateMaxFileDataFile)
Mon 16:27: (2/12) - Synthesize DFE Modules (XST)
Mon 16:30: (3/12) - Link DFE Modules (NGCBuild)
Mon 16:30: (4/12) - Prepare for Resource Analysis (EDIF2MxruBuildPass)
Mon 16:30: (5/12) - Generate Preliminary Annotated Source Code
Mon 16:30: (6/12) - Report Resource Usage (ResourceCounter)
Mon 16:30: About to start chip vendor Map/Place/Route toolflow. This will take some time.
Mon 16:30: (7/12) - Prepare for Placement (NGDBuild)
Mon 16:30: (8/12) - Place and Route DFE (MPPR)
Mon 16:30: Executing MPPR with 1 cost tables and 1 threads.
Mon 16:30: MPPR: Starting 1 cost table
Mon 16:43: MPPR: Cost table 1 met timing with score 0 (best score 0)
Mon 16:43: (9/12) - Prepare for Resource Analysis (XDLBuild)
Mon 16:44: (10/12) - Generate Resource Report (ResourceUsageBuildPass)
Mon 16:44: (11/12) - Generate Annotated Source Code (ResourceAnnotationBuildPass)
Mon 16:44: (12/12) - Generate MaxFile (GenerateMaxFile)
Mon 16:45: FINAL RESOURCE USAGE LUTs: 9503 / 149760 (6.35%) FFs: 12749 / 149760 (8.51%) BRAMs: 34 / 516 (6.59%)
chip vendor specific back-end tool flow
Abstracted by MaxCompiler

## Slide 98
Compilation: On-Chip Resources
98
Different operations use different resources
Main resources
  logic (LUTs)
  state (Flip-flops)
  27x18 bit multipliers (DSPs)
  Block RAM (36Kb) + URAM(288Kb)
  Wires and switches / Routing!
  IO for off-chip communication
DSP Block (~6800)
Block RAM (~40 MByte)
I/O Block
LUT/FF (~1m)

## Slide 99
Compilation: Resource Usage Report
99
Allows you to see which lines of code are using which resources and decide what to optimize
  Separate reports for each kernel and for the manager
LUTs FFs BRAMs DSPs : MyKernel.java
727 871 1.0 2 : resources used by this file
0.24% 0.15% 0.09% 0.10% : % of available
71.41% 61.82% 100.00% 100.00% : % of total used
94.29% 97.21% 100.00% 100.00% : % of user resources
:
: public class MyKernel extends Kernel {
: public MyKernel (KernelParameters parameters) {
: super(parameters);
1 31 0.0 0 : DFEVar p = io.input("p", dfeFloat(8,24));
2 9 0.0 0 : DFEVar q = io.input("q", dfeUInt(8));
: DFEVar offset=io.scalarInput("ost", dfeUInt(8));
8 8 0.0 0 : DFEVar addr = offset + q;
18 40 1.0 0 : DFEVar v = mem.romMapped("table", addr,
: dfeFloat(8,24), 256);
139 145 0.0 2 : p = p * p;
401 541 0.0 0 : p = p + v;
: io.output("r", p, dfeFloat(8,24));
: }
: }
dfeFloat is
expensive

## Slide 100
MaxCompiler gives detailed latency and area annotation back to the programmer
Evaluate precise effect of code
on latency and chip area
12.8ns
6.4ns
+
=
19.2ns (total compute latency)
100
Compilation: Latency Report

## Slide 101
Real data flow graph as generated by MaxCompiler
  4866 nodes
  10,000s of stages/cycles
Compilation: Dataflow Graph
101

## Slide 102
Hands on Example
10.7.2019

## Slide 103
Three shared accounts to have a first look around
https://webide.maxeler.com
Full development environment on AWS:
  MaxCompiler AMI on AWS marketplace
  https://aws.amazon.com/marketplace/pp/Maxeler-Technologies-Inc-MaxCompiler-AMI/B07K6TGWNQ
For further information contact either info@maxeler.com or nvoss@maxeler.com
Login
103
User | Password
user32 | 1275
user33 | 1158
user34 | 1342